## Slide 1
Stack
Organization

## Slide 2: STACK ORGANIZATION
Stack or LIFO(Last-In, First-Out)
oA storage device that stores information
  The item stored last is the first item retrieved = a stack of tray
oStack Pointer (SP)
  The register that holds the address for the stack
  SP always points at the top item in the stack
oTwo Operations of a stack : Insertion and Deletion of Items
  PUSH : Push-Down = Insertion
  POP : Pop-Up = Deletion

## Slide 3: TYPES OF STACK
Register Stack (Stack Depth: LIMITED) oA finite number of memory register(stand alone)
Memory Stack (Stack Depth: FLEXIBLE)
oA portion of a large memory
words or

## Slide 4: REGISTER STACK
SP  SP 1
M [SP]  DR
If (SP  0) then (FULL  1)
EMTY  0
Increment SP
: Write to the stack
: Check if stack is full
: Mark not empty
Push Operation
The first item is stored at address 1, and the last item is stored at address 0
Pop Operation
DR  M [SP]
SP  SP  1
If (SP  0) then (EMTY  1)
FULL  0
: Read item from the of stack
: Decrement Stack Pointer
: Check if stack is empty
: Mark not full

## Slide 5: EXAMPLE OF PUSH& POP OPERATION.
A
11 |  | 
10 |  | 
01 |  | 
00 | D | 
1
0
DR
FULL
EMTY
PUSH A
PUSH B
PUSH C PUSH D
1
0
FULL EMTY
POP D
D
DR

## Slide 6
MEMORY STACK
Push Operation
The first item is stored at address 4000
Pop Operation
SP  SP 1
M [SP]  DR
DR  M [SP]
SP  SP  1
Program (instructions)
Data (operands)
Stack
SP
PC
AR
DR
1000
2000
3000
3997
3998
3999
4000
4001
Address
Memory unit
Start Here

## Slide 7: RPN (Reverse Polish Notation)
The common mathematical method of writing arithmetic expressions imposes difficulties when evaluated by a computer
A stack organization is very effective for evaluating arithmetic expressions
A * B + C * D  AB * CD * +
( 3 * 4 ) + ( 5 * 6 )  34 * 56 * +
3
6
5
12
42
30
12
5
12
12
4
3
4
3
+
*
6
5
*

## Slide 8: THANK YOU!